## Slide 1: 常见弹性模型
非物理模型
质量弹簧模型(mass spring model)、质量张量模型(mass tensor model)
有限元模型(FEM)
样条方法
1. 非均匀有理样条 (nonuniform rational B-spline)
2. 动态体积样条(dynamic volume spline)

## Slide 2: 非物理模型
仅考虑人体的几何特征，运用纯几何的技术来计算物体的外形和运动。虽然计算效率高，但是不考虑体积的变化。
应用
计算机辅助设计、手术模拟的教育和培训

## Slide 3: 质量弹簧模型
原理
将形变体的物理特性离散到各个节点及节点间的弹簧上，然后在每个节点上建立运动方程。
Terzopoulous 等应用到脸部建模，模拟脸部表情
Erwin Keeve 等考虑到骨组织，用于手术模拟

## Slide 4: 质量弹簧模型
优点
结构简单，占用内存少
缺点
1. 不易控制体积守恒，并且精度不如有限元模型
2. 依赖材料参数

## Slide 5: 有限元模型
平衡方程
(总势能) = ʌ(应变) - W(外力做功)
有限元离散 (基于极小化势能原理)
选取单元、基函数、计算单元矩阵、组装 整体刚度矩阵
求解 获得节点位移，计算应力和应变

## Slide 6: 有限元模型
考虑不可压缩
应力应变关系
其中 体积模量
剪切模量
剪切应变 体积应变分量

## Slide 7: 有限元模型
优点
有限元模型与生物力学非常相关，并且 计算精度较高
缺点
相对计算量较大，占用内存多

## Slide 8: 动态体积样条
体积样条方程, 脸部的软组织模拟
: 控制点的个数
控制点 的运动方程
M: 局部质量矩阵 D: 局部弹性关系 K：局部阻尼系数矩阵

## Slide 9: 动态体积样条算例
Fig. 2. A piece of skin material segmented from
the patient’s CT data and the volume spline control points as red dots when some force is applied on the skin surface.
Fig. 1. A piece of skin material segmented
from the forehead of the patient’s CT data and the volume spline control points as red dots.

## Slide 10
Fig. 3. Presurgical face CT model (left), postsurgical face model (middle), and 3D virtual simulation result of CASS (right) for 6 different patients.
Fig. 4. Presurgical face CT model (left), post-surgical face model (middle), and 3D virtual simulation result of dynamic volume spline (right) for 6 different patients.

## Slide 11: 动态体积样条
优点
与软件CASS 对比，预测皮肤与术后皮肤的误差更小。

## Slide 12: 非均匀有理B样条